Tropical Cyclone Report

Tropical Storm Olga

(AL172007)

11 – 12 December 2007

Michelle Mainelli

National Hurricane Center

24 January 2008

Olga was a short-lived out of season tropical storm that produced torrential rains, flooding, and loss of life across portions of the Dominican Republic, Haiti, and Puerto Rico.  Olga’s remnants continued across the northwestern Caribbean Sea and into the eastern Gulf of Mexico before being absorbed by a cold front over central Florida.

- Synoptic History

# Olga’s genesis resulted from the interaction of an upper-level low with a low-level trough over the central Atlantic Ocean.  Early on 6 December, a broad upper-level low developed over the east-central Atlantic along with an associated low-level trough that stretched along 35oW between 20oN and 30oN.  These features moved westward, in tandem, at 15-20 kt uneventfully during the next couple of days. Late on 8 December, shower and thunderstorm activity developed in the vicinity of the upper-level low and surface trough.  By 10 December, a broad area of surface low pressure formed about 350 n mi east of Puerto Rico, and although thunderstorm activity remained disorganized at that time, the low produced gale force winds to the north of the center.  Around 0000 UTC 11 December, satellite imagery and radar data from San Juan, Puerto Rico WSR-88D and surface observations over the Virgin Islands indicated that the system developed a well-defined surface circulation and sufficiently organized convection relatively close to the center for the system to be designated as a subtropical storm about 50 n mi east of San Juan, Puerto Rico.  Because the surface low was still associated with a cold low aloft, the system is considered to be subtropical at this time.  In addition, the cyclone had radius of maximum winds of about 175 n mi, which is typical of subtropical cyclones.  The “best track” chart of the tropical cyclone’s path is given in Fig. 1, with the wind and pressure histories shown in Figs. 2 and 3, respectively.  The best track positions and intensities are listed in Table 1.

# Under the influence of a low- to mid-level ridge to the north, Olga moved westward along the northern coast of Puerto Rico on 11 December and made landfall along the north central coast of Puerto Rico around 0700 UTC.  Later that day, satellite imagery indicated that shower and thunderstorm activity increased near the center, and surface observations along with surface wind data from the Advanced Scatterometer (ASCAT) suggested that the radius of maximum winds had decreased.  By 1800 UTC 11 December, Olga became a tropical storm by the time it made landfall just south of Punta Cana in the Dominican Republic with a peak intensity of 50 kt.  Despite the mountainous terrain, Olga maintained its peak intensity for about 12 h while moving across eastern Hispaniola, with the strongest winds remaining offshore in the area of deepest convection.  Olga finally weakened over central Hispaniola, and by the time the cyclone emerged over the Windward Passage around 1200 UTC 12 December the intensity had decreased to 35 kt.  Olga became a tropical depression six hours later and degenerated into a remnant low the next day just north of Jamaica.

# The remnant low continued westward across the northwestern Caribbean Sea during the next couple of days.  By 15 December, the non-convective low moved northwestward and northward around the western periphery of a low- to mid-level ridge.  Later that day and early on 16 December, the remnants of Olga accelerated northeastward over the eastern Gulf of Mexico ahead of an approaching cold front, producing somewhat organized thunderstorm activity.  Satellite imagery and radar data from Tampa, Florida suggested that a small circulation crossed the west-central coast of Florida just north of Tampa around 1000 UTC 16 December.  During that time, Olga’s remnants interacted with an intense squall line that stretched across north central Florida. While post-analysis does not indicate that redevelopment into a tropical cyclone occurred, the remnants of Olga in conjunction with the cold front and pre-frontal squall line produced sustained winds of tropical storm force with gusts to hurricane force in Clearwater Beach, Florida. Within two hours of Olga’s remnants reaching the west central coast of Florida, the remnants were absorbed by the cold front.

- Meteorological Statistics

Observations in Olga (Figs. 2 and 3) include satellite-based Hebert-Poteat and Dvorak technique intensity estimates from the Tropical Analysis and Forecast Branch (TAFB) and the Satellite Analysis Branch (SAB), as well as flight-level and Stepped Frequency Microwave Radiometer (SFMR) surface observations from one mission of the 53rd Weather Reconnaissance Squadron of the U.S. Air Force Reserve Command.  Microwave satellite imagery from NOAA polar-orbiting satellites, the NASA Tropical Rainfall Measuring Mission (TRMM), the NASA Aqua, the NASA QuikSCAT, the Department of Defense WindSat, ASCAT, and Defense Meteorological Satellite Program (DMSP) satellites were also useful in tracking Olga. Conventional land-based surface observations, buoys, and National Weather Service Doppler radar data were helpful in tracking the path of Olga.

The estimated 50 kt peak intensity of Olga while it was making landfall over the Dominican Republic early on 12 December is based on a blend of the surface-adjusted flight-level winds and SFMR data from U.S. Air Force aircraft.  Peak flight-level winds measured by the plane were 55 kt, corresponding to 44 kt at the surface.  There was an SFMR surface report of 54 kt, but this measurement was determined to be too high due to shoaling along the coast. A couple of  SFMR measurements, however, indicated surface winds around 47 kt  prior to the aircraft reaching the shallow waters just north of the Dominican Republic.

The primary impact of Olga was the heavy rainfall that affected portions of Puerto Rico and the island of Hispaniola.  Maximum rainfall totals across the region ranged from around 11 inches in central Puerto Rico to over 15 inches in the Dominican Republic.  Figure 4 shows the rainfall distribution across Puerto Rico.  Tropical storm force winds were present north of the center during both the subtropical and tropical stages of Olga.  While several ship reports from 11 – 12 December across the Southwestern Atlantic Ocean measured tropical storm force winds, these winds were due to a strong environmental pressure gradient and were not directly associated with the circulation of Olga.  Table 2 provides a summary of selected ship observations that reported sustained winds of tropical storm force directly associated with Olga, and Table 3 provides a summary of rainfall totals.

- Casualty and Damage Statistics

Due primarily to torrential rainfall, mudslides, and flooding of the Yaque River in the Dominican Republic, at least 22 deaths are directly associated with Olga in that country, according to the Dominican Republic Meteorological Office.  In addition, 2 deaths in Haiti and 1 death in Puerto Rico were reported in association with Olga. Olga’s impact was unusually severe due to the grounds having been previously saturated from the passage of Tropical Storm Noel at the end of October. News reports indicate that almost 12,000 homes were damaged, including 370 that were completely destroyed, which caused more than 60,000 people to be displaced.  During the time when Olga’s remnants moved rapidly across Florida, a tornado touched down in central Florida in Pasco County causing damage to several buildings including a County Fire Station and the Pasco County Jail.

- Forecast and Warning Critique

Olga developed outside of the official hurricane season and Tropical Weather Outlook (TWO) statements were not being routinely generated; however, Special Tropical Disturbance Statements (DSA) were issued beginning at 2200 UTC 9 December, about 26 hours prior to genesis.  In total, six DSAs were disseminated by NHC prior to the first advisory issuance and all statements indicated that tropical or subtropical cyclone formation could occur.

A verification of NHC official and guidance model track forecasts can be found in Table 4.  Since Olga was a short-lived cyclone, very few forecasts verified.  The number of forecasts ranged from six at 12 h to two at 36 h. The average official track errors for Olga were 47, 61, and 52 n mi for the 12, 24, and 36 h forecasts, respectively.  These errors are close to the average long-term official track errors.

Average NHC official intensity errors were 7, 9, and 5 kt for the 12, 24, and 36 h forecasts, respectively (Table 5).  For comparison, the average long-term official intensity errors are 6, 10, and 12 kt, respectively.   The official intensity forecast errors were below or near the average long-term errors at each forecast time.

Due to the close proximity of Olga’s genesis to Hispaniola, tropical storm warnings and watches were issued in the first advisory early on 11 December.  Even though the center of Olga moved across northwestern Puerto Rico, watches and warnings were not necessary for the island as the tropical storm force winds were confined to the north of the center and rainfall was the primary threat.  Table 6 provides a summary of the watches and warnings issued in association with Olga.

e.	Acknowledgements:

Observations from the Dominican Republic were provided by the Dominican Republic Meteorological Office. Lixion Avila and Daniel Brown from NHC, Roham Abtahi from WFO/SJU, and David Roth from HPC assisted in the compilation of the observation table.  Colin McAdie (NHC) provided access to and analysis of archived WSR-88D radar data from the WFO in Tampa, Florida. Roger Edwards (SPC) and Jiann-Gwo Jiing (NHC) provided valuable insight of the remnants of Olga as it moved across the eastern Gulf of Mexico and across Florida. I would also like to thank my colleagues at NHC for their valuable suggestions to this report.

Table 1.	Best track for Tropical Storm Olga, 11-12 December 2007.

| Date/Time (UTC) | Latitude ((N) | Longitude ((W) | Pressure (mb) | Wind Speed (kt) | Stage |
| --- | --- | --- | --- | --- | --- |
| 10 / 1200 | 18.3 | 61.8 | 1009 | 35 | low |
| 10 / 1800 | 18.3 | 63.2 | 1008 | 35 | " |
| 11 / 0000 | 18.4 | 64.7 | 1007 | 35 | subtropical storm |
| 11 / 0600 | 18.5 | 66.3 | 1005 | 40 | " |
| 11 / 1200 | 18.3 | 67.4 | 1004 | 45 | " |
| 11 / 1800 | 18.5 | 68.4 | 1003 | 50 | tropical storm |
| 12 / 0000 | 19.0 | 70.0 | 1003 | 50 | " |
| 12 / 0600 | 19.1 | 71.9 | 1005 | 40 | " |
| 12 / 1200 | 19.1 | 73.8 | 1008 | 35 | " |
| 12 / 1800 | 19.0 | 75.7 | 1008 | 30 | tropical depression |
| 13 / 0000 | 18.9 | 77.2 | 1008 | 30 | remnant low |
| 13 / 0600 | 19.0 | 78.7 | 1007 | 30 | " |
| 13 / 1200 | 19.4 | 80.1 | 1007 | 30 | " |
| 13 / 1800 | 19.6 | 81.3 | 1007 | 30 | " |
| 14 / 0000 | 19.7 | 82.3 | 1007 | 30 | " |
| 14 / 0600 | 19.7 | 83.3 | 1007 | 30 | " |
| 14 / 1200 | 19.6 | 84.2 | 1007 | 30 | " |
| 14 / 1800 | 19.5 | 85.1 | 1007 | 30 | " |
| 15 / 0000 | 20.0 | 85.8 | 1006 | 30 | " |
| 15 / 0600 | 20.6 | 86.5 | 1006 | 30 | " |
| 15 / 1200 | 21.7 | 87.4 | 1007 | 30 | " |
| 15 / 1800 | 23.3 | 88.2 | 1007 | 30 | " |
| 16 / 0000 | 25.0 | 87.2 | 1005 | 30 | " |
| 16 / 0600 | 26.3 | 85.2 | 1006 | 25 | " |
| 16 / 1000 | 28.2 | 82.7 | 1003 | 30 | remnant low crossed Florida west coast just north of Tampa |
| 16 / 1200 |  |  |  |  | merged with frontal system |
| 11 / 1800 | 18.5 | 68.4 | 1003 | 50 | minimum pressure |
| 11 / 0700 | 18.4 | 66.5 | 1005 | 40 | landfall north central Puerto Rico just west of Vega Baha |
| 11 / 1800 | 18.5 | 68.4 | 1003 | 50 | landfall just south of Punta Cana, Dominican Republic |

Table 2.	Selected ship reports with winds of at least 34 kt for Tropical Storm Olga, 11-12 December, 2007.

| Date/Time (UTC) | Ship call sign | Latitude ((N) | Longitude ((W) | Wind Dir/speed (kt) | Pressure (mb) |
| --- | --- | --- | --- | --- | --- |
| 11/0000 | PFRO | 19.1 | 67.8 | 090 / 35 | 1013.0 |
| 11/0300 | PBIG | 19.9 | 67.8 | 030 / 37 | 1010.0 |
| 11/0600 | A8EG8 | 19.2 | 66.3 | 040 / 41 | 1012.3 |
| 11/1200 | PBIG | 19.3 | 65.9 | 080 / 45 | 1008.0 |
| 11/1300 | PFRO | 20.8 | 68.4 | 080 / 45 | 1012.6 |
| 11/1500 | WJBJ | 20.8 | 66.5 | 090 / 35 | 1014.9 |
| 11/1900 | PFRO | 20.3 | 68.3 | 070 / 51 | 1010.5 |
| 11/2300 | ZCDG8 | 21.2 | 68.3 | 090 / 40 | 1015.9 |
| 12/0000 | PINX | 19.7 | 69.0 | 060 / 51 | 1014.0 |
| 12/0000 | C6FV9 | 20.9 | 69.0 | 090 / 36 | 1016.0 |

Table 3.	Selected surface observations for Tropical Storm Olga, 11-12 December 2007.

| Location | Minimum Sea Level Pressure | Maximum Surface Wind Speed | Storm surge (ft)c | Storm tide (ft)d | Total rain (in) |
| --- | --- | --- | --- | --- | --- |
|  | Date/ time (UTC) | Press. (mb) | Date/ time (UTC)a | Sustained (kt)b | Gust (kt) |  |  |  |
| Dominican Republice |  |  |  |  |  |  |  |  |
| Altamira |  |  |  |  |  |  |  | 6.52 |
| Angelina |  |  |  |  |  |  |  |  |
| Arroyo Barril |  |  |  |  |  |  |  | 3.70 |
| Azua |  |  |  |  |  |  |  | 6.66 |
| Bani |  |  |  |  |  |  |  | 6.73 |
| Barahona |  |  |  |  |  |  |  | 4.87 |
| Bayaguana (78473) | 12/0000 | 1007.6 |  |  |  |  |  | 2.63 |
| Bohechio |  |  |  |  |  |  |  | 2.36 |
| Bonao |  |  |  |  |  |  |  | 7.44 |
| Cabrera |  |  |  |  |  |  |  | 3.37 |
| Catey Airport |  |  | 11/2300 |  | 55 |  |  | 4.65 |
| Constanza |  |  |  |  |  |  |  | 4.94 |
| Cotui |  |  |  |  |  |  |  | 6.94f |
| Dajabon |  |  |  |  |  |  |  | 2.37 |
| Duverge |  |  |  |  |  |  |  | 4.17 |
| El Cercado |  |  |  |  |  |  |  | 1.95 |
| Elias Pina |  |  |  |  |  |  |  | 0.89 |
| Gaspar Hdez |  |  |  |  |  |  |  | 3.20 |
| Hato Mayor |  |  |  |  |  |  |  | 1.45 |
| Herrera (78484) | 11/2300 | 1006.0 |  |  |  |  |  |  |
| Higuey |  |  |  |  |  |  |  | 4.25 |
| Jarabacoa |  |  |  |  |  |  |  | 8.92f |
| Joaquin Balaguer Airport |  |  |  |  |  |  |  | 4.96 |
| Juma Bonao |  |  |  |  |  |  |  | 7.35 |
| La Descubierta |  |  |  |  |  |  |  | 0.98 |
| La Romana | 11/2100 | 1004.7 |  |  |  |  |  | 1.94 |
| La Union (Airport) |  |  |  |  |  |  |  | 7.18 |
| La Vega |  |  |  |  |  |  |  | 6.30 |
| Las Americas (78485) | 12/0000 | 1007.0 |  |  |  |  |  | 3.50 |
| Las Matas de Cruz |  |  |  |  |  |  |  | 2.38f |
| Limon del Yuna |  |  |  |  |  |  |  | 4.78 |
| Loma Cabrera |  |  |  |  |  |  |  | 1.50 |
| Los Llanos |  |  |  |  |  |  |  | 0.99 |
| Luperon |  |  |  |  |  |  |  | 3.12 |
| Mao |  |  |  |  |  |  |  | 2.38 |
| Miches |  |  |  |  |  |  |  | 1.20 |
| Moca |  |  |  |  |  |  |  | 8.32 |
| Moncion |  |  |  |  |  |  |  | 2.84 |
| Monte Cristi |  |  |  |  |  |  |  | 1.58 |
| Monte Plata |  |  |  |  |  |  |  | 5.11 |
| Nagua |  |  |  |  |  |  |  | 2.93 |
| Neyba |  |  |  |  |  |  |  | 3.89 |
| Oviedo |  |  |  |  |  |  |  | 2.18 |
| Padre Las Casas |  |  |  |  |  |  |  | 3.03 |
| Pimentel |  |  |  |  |  |  |  | 2.50 |
| Polo |  |  |  |  |  |  |  | 15.32 |
| Puerto Plata (78458) | 12/0300 | 1010.0 | 12/0300 |  | 35 |  |  |  |
| Punta Cana (78479) | 11/1300 | 1003.0 | 11/1300 | 35 |  |  |  | 5.65 |
| Rancho Arriba |  |  |  |  |  |  |  | 10.05f |
| Restauracion |  |  |  |  |  |  |  | 1.89 |
| Rio San Juan |  |  |  |  |  |  |  | 7.40 |
| S.G. Boya |  |  |  |  |  |  |  | 5.35 |
| Sabana De La Mar (78467) | 11/2100 | 1006.7 |  |  |  |  |  | 3.01 |
| Salcedo |  |  |  |  |  |  |  | 4.61 |
| Samana |  |  |  |  |  |  |  | 3.04 |
| San Cristobal |  |  |  |  |  |  |  | 5.79 |
| San Jose Ocoa |  |  |  |  |  |  |  | 7.48 |
| San Juan de la Maguana |  |  |  |  |  |  |  | 1.66 |
| San Rafael Del Yuma |  |  |  |  |  |  |  | 4.13 |
| Sanchez |  |  |  |  |  |  |  | 3.28 |
| Santiago (78460) | 12/0300 | 1008.0 | 12/0300 | 20 | 25 |  |  | 7.48 |
| Santo Domingo (78488) | 11/2100 | 1007.6 |  |  |  |  |  | 4.92 |
| STGO. Rodriguez |  |  |  |  |  |  |  | 1.93 |
| Villa Altagracia |  |  |  |  |  |  |  | 1.91 |
| Villa Riva |  |  |  |  |  |  |  | 6.72 |
| Villa Vasquez |  |  |  |  |  |  |  | 2.91f |
| Yamasa |  |  |  |  |  |  |  | 7.19f |
| Puerto Rico and Virgin Islands |  |  |  |  |  |  |  |  |
| St. Thomas Airport (78543) |  |  | 10/1153 |  | 42 |  |  |  |
| San Juan Airport (78526) |  |  | 11/0426 |  | 32 |  |  |  |
| Ponce, Rio Cerrillos above Lago Cerrillos |  |  |  |  |  |  |  | 11.13 |
| Villalba |  |  |  |  |  |  |  | 9.54 |
| Rio Matrullas |  |  |  |  |  |  |  | 7.80 |
| Rio Toa Vaca above Dam |  |  |  |  |  |  |  | 7.26 |
| Rio Grande de Loiza, San Lorenzo |  |  |  |  |  |  |  | 6.93 |
| Rio Jacaquas-Villalba |  |  |  |  |  |  |  | 6.72 |
| Vaqueria el Nimo, Caguas |  |  |  |  |  |  |  | 6.26 |
| Canaboncito, Caguas/Aguas Buenas |  |  |  |  |  |  |  | 6.23 |
| Bairoa Arriba, Aguas Buenas |  |  |  |  |  |  |  | 6.06 |
| Rio Bayamon @ Arenas, Cidra |  |  |  |  |  |  |  | 5.92 |
| Queb Blanco, San Lorenzo |  |  |  |  |  |  |  | 5.35 |
| Lago Toa Vaca |  |  |  |  |  |  |  | 5.24 |
| Rio Bayamon, Cidra |  |  |  |  |  |  |  | 5.23 |
| Rio Bauta, Orocovis |  |  |  |  |  |  |  | 5.15 |
| Lago Carite, Guayama |  |  |  |  |  |  |  | 5.05 |
| Rio Saliente, Jayuya |  |  |  |  |  |  |  | 4.87 |
| Ponce North |  |  |  |  |  |  |  | 4.62 |
| Rio Guanajibo-Sabana Grande |  |  |  |  |  |  |  | 4.26 |
| Bahamas |  |  |  |  |  |  |  |  |
| Turks Island (78118) |  |  | 12/0316 | 34 |  |  |  |  |
| Buoys |  |  |  |  |  |  |  |  |
| 41043 – Southwestern Atlantic (21.0°N 65.1°W) | 11/0350 | 1012.3 | 02/0616 | 37g | 49 |  |  |  |

a  Date/time is for sustained wind when both sustained and gust are listed.

b  Except as noted, sustained wind averaging periods for C-MAN and land-based ASOS reports are 2 min; buoy averaging periods are 8 min.

c  Storm surge is water height above normal astronomical tide level.

d  Storm tide is water height above National Geodetic Vertical Datum (1929 mean sea level).

e  Rainfall totals from the Dominican Republic are accumulations between 11-12 December. All information received from the Dominican Republic Meteorological Office

f  Incomplete.

g  1-min average.

Table 4.	Preliminary track forecast evaluation (heterogeneous sample) for Tropical Storm Olga, 11-12 December 2007.  Forecast errors (n mi) are followed by the number of forecasts in parentheses.  Errors smaller than the NHC official forecast are shown in bold-face type.  Verification includes the depression stage but does not include the remnant low stage.

| Forecast Technique | Forecast Period (h) |
| --- | --- |
|  | 12 | 24 | 36 | 48 | 72 | 96 | 120 |
| CLP5 | 64 (6) | 84 (4) | 147 (2) |  |  |  |  |
| GFNI | 184 (3) | 359 (1) |  |  |  |  |  |
| GFDI | 46 (6) | 48 (4) | 34 (2) |  |  |  |  |
| HWFI | 42 (6) | 47 (4) | 48 (2) |  |  |  |  |
| GFSI | 49 (5) | 66 (3) | 82 (1) |  |  |  |  |
| AEMI | 48 (6) | 64 (4) | 59 (2) |  |  |  |  |
| NGPI | 51 (5) | 133 (3) | 181 (2) |  |  |  |  |
| UKMI | 40 (4) | 27 (2) | 80 (1) |  |  |  |  |
| BAMD | 101 (6) | 182 (4) | 269 (4) |  |  |  |  |
| BAMM | 43 (6) | 46 (4) | 74 (2) |  |  |  |  |
| BAMS | 43 (6) | 66 (4) | 91 (2) |  |  |  |  |
| CONU | 53 (6) | 74 (4) | 83 (2) |  |  |  |  |
| GUNA | 51 (2) | 72 (1) | 42 (1) |  |  |  |  |
| FSSE | 49 (5) | 61 (3) | 76 (1) |  |  |  |  |
| OFCL | 47 (6) | 61 ( 4) | 52 ( 2) |  |  |  |  |
| NHC Official (2002-2006 mean) | 35 (1852) | 61 (1686) | 86 (1519) | 112 (1362) | 162 (1100) | 221 (885) | 290 (723) |

Table 5.	Preliminary intensity forecast evaluation (heterogeneous sample) for Tropical Storm Olga, 11-12 December 2007.  Forecast errors (kt) are followed by the number of forecasts in parentheses.  Errors smaller than the NHC official forecast are shown in bold-face type.  Verification includes the depression stage but does not include the remnant low stage.

| Forecast Technique | Forecast Period (h) |
| --- | --- |
|  | 12 | 24 | 36 | 48 | 72 | 96 | 120 |
| SHF5 | 10.3 (6) | 10.0 (4) | 9.5 (2) |  |  |  |  |
| GHMI | 6.8 (6) | 8.5 (4) | 15.0 (2) |  |  |  |  |
| HWFI | 8.0 (6) | 8.3 (4) | 6.5 (2) |  |  |  |  |
| SHIP | 10.2 (6) | 5.5 (4) | 4.5 (2) |  |  |  |  |
| DSHP | 10.2 (6) | 7.0 (4) | 4.0 (2) |  |  |  |  |
| FSSE | 10.8 (5) | 6.0 (3) | 8.0 (1) |  |  |  |  |
| ICON | 8.0 (6) | 7.0 (4) | 4.5 (2) |  |  |  |  |
| OFCL | 6.7 (6) | 8.8 (4) | 5.0 (2) |  |  |  |  |
| NHC Official (2002-2006 mean) | 6.4 (1852) | 9.8 (1686) | 12.0 (1519) | 14.1 (1362) | 18.3 (1100) | 19.8 (885) | 21.8 (723) |

Table 6.	Watch and warning summary for Tropical Storm Olga, 11 – 12 December, 2007.

| Date/Time (UTC) | Action | Location |
| --- | --- | --- |
| 11 / 0300 | Tropical Storm Warning issued | Northern coast of the Dominican Republic from Cabo Engano to Bahio de Manzanillo |
| 11 / 0300 | Tropical Storm Watch issued | Southern coast of the Dominican Republic from Cabo Engano to Punta Palenque |
| 11 / 1500 | Tropical Storm Warning extended | Extended westward to include the entire northern coasts of the Dominican Republic and Haiti |
| 11 / 1800 | Tropical Storm Warning issued | Southeastern Bahamas and the Turks and Caicos Islands |
| 12 / 1500 | Tropical Storm Warnings discontinued | Dominican Republic and Haiti |
| 12 / 1500 | Tropical Storm Watch discontinued | Dominican Republic |
| 12 / 2100 | Tropical Storm Warning discontinued | Southeastern Bahamas and the Turks and Caicos Islands |

Figure 1.	Best track positions for Tropical Storm Olga, 11- 12 December 2007.

Figure 2.	Selected wind observations and best track maximum sustained surface wind speed curve for Tropical Storm Olga, 11-12 December 2007.

Figure 3.	Selected pressure observations and best track minimum central pressure curve for Tropical Storm Olga, 11-12 December 2007.

Figure 4.	Storm total precipitation associated with Olga and its pre-formation stage over Puerto Rico.  Figure courtesy of David Roth at the Hydrometeorological Prediction Center, Camp Springs, MD.